[This foreword and the “Overview” on the following pages are not part of this Test Package. They are merely informative and do not contain requirements necessary for conformance to the Test Package.]

FOREWORD

The purpose of this addendum is to present current changes being made to the BTL Test Package. These modifications are the result of change proposals made pursuant to the continuous maintenance procedures and of deliberations within the BTL-WG Committee. The changes are summarized below.

BTL-15.0b-1 Extend Checklist to contain all current standard functionality, p. 2 [BTLWG-342]

In the following document, language to be added to existing clauses within the BTL Test Package 15.0 is indicated through the use of italics, while deletions are indicated by strikethrough. Where entirely new subclauses are proposed to be added, plain type is used throughout

In addition, changes to BTL Specified Tests also contain a yellow highlight to indicate the changes made by this addendum.

When this addendum is applied, all highlighting will be removed.  Change markings on tests will remain to indicate the difference between the new test and an existing 135.1 test.  If a test being modified has never existed in 135.1, the applied result should not contain any change markings.  When this is the case, square brackets will be used to describe the changes required for this test.

Each addendum can stand independently unless specifically noted via dependency within the addendum.  If multiple addenda change the same test or section, each future released addendum that changes the same test or section will note in square brackets whether or not those changes are reflected.

BTL-15.0b-1:  Extend Checklist to contain all current standard functionality

Overview:

The checklist needs to be updated to contain all objects and BIBBs currently defined in 135.  This will carry the checklist up to Protocol_Revision 19.

Objects and BIBBs that are listed below are listed in order of 135-2016.

Changes:

[In BTL Checklist, add these objects to end of Objects Section]

| Support | Listing | Option |
| --- | --- | --- |
| Program Object |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this object. |
| Life Safety Point Object |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this object. |
| Life Safety Zone Object |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this object. |
| Pulse Converter Object |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this object. |
| Access Door Object |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this object. |
| Load Control Object |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this object. |
| Access Point Object |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this object. |
| Access Zone Object |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this object. |
| Access User Object |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this object. |
| Access Rights Object |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this object. |
| Access Credential Object |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this object. |
| Credential Data Input Object |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this object. |
| Network Security Object |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this object. |
| Notification Forwarder Object |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this object. |
| Alert Enrollment Object |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this object. |
| Channel Object |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this object. |
| Lighting Output Object |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this object. |
| Binary Lighting Output Object |
|  | R1,2 | Base Requirements |
| 1Contact BTL for interim tests for this object. 2Protocol_Revision 16 or higher must be claimed |
| Network Port Object |
|  | R1,2 | Base Requirements |
| 1Contact BTL for interim tests for this object. 2Protocol_Revision 17 or higher must be claimed |
| Timer Object |
|  | R1,2 | Base Requirements |
| 1Contact BTL for interim tests for this object. 2Protocol_Revision 17 or higher must be claimed |
| Elevator Group Object |
|  | R1,2 | Base Requirements |
| 1Contact BTL for interim tests for this object. 2Protocol_Revision 18 or higher must be claimed |
| Lift Object |
|  | R1,2 | Base Requirements |
| 1Contact BTL for interim tests for this object. 2Protocol_Revision 18 or higher must be claimed |
| Escalator Object |
|  | R1,2 | Base Requirements |
| 1Contact BTL for interim tests for this object. 2Protocol_Revision 18 or higher must be claimed |

[In BTL Checklist, modify the following BIBBs to include the new sections.  They should be added directly below the last Conditional entry and before the Optional entry.]

| Data Sharing - COV - A |
| --- |
| . . . |
|  | C2 | Can subscribe for COV from Pulse Converter objects |
|  | C2 | Can subscribe for COV from Access Door objects |
|  | C2 | Can subscribe for COV from Load Control objects |
|  | C2 | Can subscribe for COV from Access Point objects |
|  | C2 | Can subscribe for COV from Credential Data Input objects |
|  | C2 | Can subscribe for COV from Lighting Output objects |
|  | C2,3,4 | Can subscribe for COV from Binary Lighting Output objects |
| . . . |
| 3Contact BTL for interim tests for this object. 4Protocol_Revision 16 or higher must be claimed. |
| Data Sharing - COV - B |
| . . . |
|  | C1 | Supports COV for Pulse Converter objects |
|  | C1 | Supports COV for Access Door objects |
|  | C1 | Supports COV for Load Control objects |
|  | C1 | Supports COV for Access Point objects |
|  | C1 | Supports COV for Credential Data Input objects |
|  | C1 | Supports COV for Lighting Output objects |
|  | C1,2,3 | Supports COV for Binary Lighting Output objects |
| . . . |
| 2Contact BTL for interim tests for this object. 3Protocol_Revision 16 or higher must be claimed. |

[In BTL Checklist, add the following BIBBs to the end of the Data Sharing Section]

| Data Sharing - COVP - B |
| --- |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Data Sharing - WriteGroup - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Data Sharing - WriteGroup - I - B |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Data Sharing - WriteGroup - E - B |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Data Sharing - Value Source Information - B |
|  | R1,2 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. 2Protocol_Revision 17 or higher must be claimed. |
| Data Sharing - Change Of Value Multiple - A |
|  | R1,2 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. 2Protocol_Revions 18 or higher must be claimed. |
| Data Sharing - Change Of Value Multiple - B |
|  | R1,2 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. 2Protocol_Revision 18 or higher must be claimed. |
| Data Sharing - Life Safety View - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Data Sharing - Life Safety Advanced View - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Data Sharing - Life Safety Modify - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Data Sharing - Life Safety Advanced Modify - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Data Sharing - Access Control View - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Data Sharing - Access Control Advanced View - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Data Sharing - Access Control Modify - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Data Sharing - Access Control Advanced Modify - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Data Sharing - Access Control User Configuration - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Data Sharing - Access Control User Configuration - B |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Data Sharing - Access Control Site Configuration - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Data Sharing - Access Control Site Configuration - B |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Data Sharing - Access Control Access Door - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Data Sharing - Access Control Access Door - B |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Data Sharing - Access Control Credential Data Input - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Data Sharing - Access Control Credential Data Input - B |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |

[In BTL Checklist, modify the following BIBBs to include the new sections. The AE-N-A sections should be added to the end of the BIBB.  The others should be added directly below the last Conditional entry and before any Optional entry.]

| Alarm and Event - Notification - A |
| --- |
| . . . |
|  | R | Processes CHANGE_OF_LIFE_SAFETY |
|  | R | Processes ACCESS_EVENT |
|  | R4 | Processes CHANGE_OF_DISCRETE_VALUE |
|  | R4 | Processes CHANGE_OF_TIMER |
| ... 4 Required if the device implements protocol revision 17 or higher. |
| Alarm and Event - Notification - Internal - B |
| . . . |
|  | C3 | Implements the CHANGE_OF_LIFE_SAFETY algorithm |
|  | C3 | Implements the ACCESS_EVENT algorithm |
|  | C3,5 | Implements the CHANGE_OF_DISCRETE_VALUE algorithm |
|  | C3,5,6 | Implements the CHANGE_OF_TIMER algorithm |
| . . . |
| ... 5Contact BTL for interim tests for this object. 6Protocol_Revision 17 or higher must be claimed. |
| Alarm and Event - Notification - External - B |
| . . . |
|  | C1 | Implements the CHANGE_OF_LIFE_SAFETY algorithm |
|  | C1 | Implements the ACCESS_EVENT algorithm |
|  | C1,2,3 | Implements the CHANGE_OF_DISCRETE_VALUE algorithm |
|  | C1,2,3 | Implements the CHANGE_OF_TIMER algorithm |
| . . . |
| ... 2Contact BTL for interim tests for this object. 3Protocol_Revision 17 or higher must be claimed. |

[In BTL Checklist, add the following BIBBs to the end of the Alarm and Event Management Section]

| Alarm and Event management - LifeSafety - A |
| --- |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Alarm and Event management - LifeSafety - B |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Alarm and Event management - Notification Forwarder - B |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Alarm and Event management - Notification Forwarder - I - B |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Alarm and Event management - Configurable Recipient Lists - B |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Alarm and Event management - Temporary Event Subscription - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Alarm and Event management - Life Safety View Notifications - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Alarm and Event management - Life Safety Adbanced View Notifications - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Alarm and Event management - Life Safety View and Modify - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Alarm and Event management - Life Safety Advanced View and Modify - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Alarm and Event management - Access Control - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Alarm and Event management - Access Control - B |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Alarm and Event management - Access Control Advanced View Notifications - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Alarm and Event management - Access Control View and Modify - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Alarm and Event management - Access Control Advanced View and Modify - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |

[In BTL Checklist, add the following BIBBs to the end of the Scheduling Section]

| Scheduling - Timer - I - B |
| --- |
|  | R1,2 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. 2Protocol_Revision 17 or higher must be claimed. |
| Scheduling - Timer - E - B |
|  | R1,2 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. 2Protocol_Revision 17 or higher must be claimed. |

[In BTL Checklist, modify the following BIBBs by adding the new sections, these new conditional sections should be added after the last Conditional but before the Optional section]

| Device Management - Object Creation and Deletion - A |
| --- |
| . . . |
|  | C2 | Can create and delete Access Point objects |
|  | C2 | Can create and delete Access Zone objects |
|  | C2 | Can create and delete Access User objects |
|  | C2 | Can create and delete Access Rights objects |
|  | C2 | Can create and delete Access Credential objects |
|  | C2 | Can create and delete Credential Data objects |
|  | C2 | Can create and delete Notification Forwarder objects |
|  | C2 | Can create and delete Alert Enrollment objects |
|  | C2 | Can create and delete Channel objects |
|  | C2 | Can create and delete Lighting Output objects |
|  | C2,3,6 | Can create and delete Binary Lighting Output objects |
|  | C2,4,6 | Can create and delete Network Port objects |
|  | C2,4,6 | Can create and delete Timer objects |
|  | C2,5,6 | Can create and delete Elevator Group objects |
|  | C2,5,6 | Can create and delete Lift objects |
|  | C2,5,6 | Can create and delete Escalator objects |
| . . . |
| ... 3Protocol_Revision 16 or higher must be claimed. 4Protocol_Revision 17 or higher must be claimed. 5Protocol_Revision 18 or higher must be claimed. 6Contact BTL for interim tests for this object. |
| Device Management - Object Creation and Deletion - B |
| . . . |
|  | C1 | Supports object creation and deletion of the Access Point object |
|  | C1 | Supports object creation and deletion of the Access Zone object |
|  | C1 | Supports object creation and deletion of the Access User object |
|  | C1 | Supports object creation and deletion of the Access Rights object |
|  | C1 | Supports object creation and deletion of the Access Credential object |
|  | C1 | Supports object creation and deletion of the Credential Data object |
|  | C1 | Supports object creation and deletion of the Notification Forwarder object |
|  | C1 | Supports object creation and deletion of the Alert Enrollment object |
|  | C1 | Supports object creation and deletion of the Channel object |
|  | C1 | Supports object creation and deletion of the Lighting Output object |
|  | C1,2,5 | Supports object creation and deletion of the Binary Lighting Output object |
|  | C1,3,5 | Supports object creation and deletion of the Network Port object |
|  | C1,3,5 | Supports object creation and deletion of the Timer object |
|  | C1,4,5 | Supports object creation and deletion of the Elevator Group object |
|  | C1,4,5 | Supports object creation and deletion of the Lift object |
|  | C1,4,5 | Supports object creation and deletion of the Escalator object |
| . . . |
| ... 2Protocol_Revision 16 or higher must be claimed. 3Protocol_Revision 17 or higher must be claimed. 4Protocol_Revision 18 or higher must be claimed. 5Contact BTL for interim tests for this object. |
| Device Management - List Manipulation - A |
| . . . |
|  | C1 | Supports adding and removing Device / VT_Classes_Supported entries |
|  | C1 | Supports adding and removing Device / Active_VT_Sessions entries |
|  | C1 | Supports adding and removing Life Safety Zone / Zone_Members entries |
|  | C1 | Supports adding and removing Notification Forwarder / Recipient_List entries |
|  | C1 | Supports adding and removing Notification Forwarder / Subscribed_Recipients entries |
|  | C1 | Supports adding and removing Access Door / Masked_Alarm_Values entries |
|  | C1 | Supports adding and removing Access Door / Alarm_Values entries |
|  | C1 | Supports adding and removing Access Door / Fault_Values entries |
|  | C1 | Supports adding and removing Access Point / Access_Alarm_Events entries |
|  | C1 | Supports adding and removing Access Point / Access_Transaction_Events entries |
|  | C1 | Supports adding and removing Access Point / Failed_Attempt_Events entries |
|  | C1 | Supports adding and removing Access Zone / Credentials_In_Zone entries |
|  | C1 | Supports adding and removing Access Zone / Entry_Points entries |
|  | C1 | Supports adding and removing Access Zone / Exit_Points entries |
|  | C1 | Supports adding and removing Access Zone / Alarm_Values entries |
|  | C1 | Supports adding and removing Access User / Members entries |
|  | C1 | Supports adding and removing Access User / Member_Of entries |
|  | C1 | Supports adding and removing Access User / Credentials entries |
|  | C1 | Supports adding and removing Access Credential / Authorization_Exemptions entries |
|  | C1 | Supports adding and removing Access Credential / Reason_For_Disable entries |
|  | C1,2,4 | Supports adding and removing Network Port / BBMD_Broadcast_Distribution_Table entries |
|  | C1,2,4 | Supports adding and removing Network Port / Manual_Slave_Address_Binding entries |
|  | C1,2,4 | Supports adding and removing Network Port / Virtual_MAC_Address_Table entries |
|  | C1,2,4 | Supports adding and removing Network Port / Slave_Address_Binding entries |
|  | C1,2,4 | Supports adding and removing Timer / List_Of_Object_Property_References entries |
|  | C1,2,4 | Supports adding and removing Timer / Alarm_Values entries |
|  | C1,3,4 | Supports adding and removing Device / Active_COV_Multiple_Subscriptions entries |
|  | C1,3,4 | Supports adding and removing Lift / Fault_Signals entries |
|  | C1,3,4 | Supports adding and removing Escalator / Fault_Signals entries |
|  | C1,3,4 | Supports adding and removing Elevator Group / Landing_Calls entries |
| ... 2Protocol_Revision 17 or higher must be claimed. 3Protocol_Revision 18 or higher must be claimed. 4Contact BTL for interim tests for this object. |

[In BTL Checklist, add the following BIBBs to the end of the Device and Network Management Section]

| Device Management - Virtual Terminal - A |
| --- |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Device Management - Virtual Terminal - B |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Device Management - Slave Proxy - View and Modify - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Device Management - Slave Proxy - B |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |

[In BTL Checklist, add the following BIBBs to the end of the Network Management Section]

| Network Management - Connection Establishment - A |
| --- |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Network Management - Connection Establishment - B |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Network Management - Router Configuration - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Network Management - BBMD Configuration - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Network Management - BBMD Configuration - B |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Network Management - Foreign Device Registration - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |

[In BTL Checklist, add the new section and BIBBs following the Network Management Section]

# Gateway

| Support | Listing | Option |
| --- | --- | --- |
| Gateway - Virtual Network - B |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Gateway - Embedded Objects - B |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |

[In BTL Checklist, add the new section and BIBBs following the Gateway Section]

# Network Security BIBBs

| Support | Listing | Option |
| --- | --- | --- |
| Network Security - Secure Device |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Network Security - Encrypted Device |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Network Security - Multi-Application Device |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Network Security - Device Master Key - A |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Network Security - Device Master Key - B |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Network Security - Encrypted Device |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Network Security - Key Server |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Network Security - Temporary Key Server |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Network Security - Secure Router |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |
| Network Security - Security Proxy |
|  | R1 | Base Requirements |
| 1Contact BTL for interim tests for this BIBB. |